## Slide 1: Moving Beyond Manual Counting How Automated License Plate Recognition-Based Occupancy Studies can Help Cities Evaluate Parking Policy
T2 Connect Conference
Brett Wood, Kimley-Horn
November 17, 2015

## Slide 2: Agenda
Traditional LPR use
Traditional data collection processes
LPR as a Data Collection Tool
  The Kimley-Horn Pilot Test
  Challenges
  The “Ah Ha” Moment
Practical Applications
  Enhancing the process
Improving the Technology for Everyone

## Slide 3: Traditional Approaches and Tools

## Slide 4: Traditional Approaches to Data Collection
  Manual data collection
  Video data collection
  Counters and sensors
  Revenue control equipment
  Advanced approaches

## Slide 5: Traditional LPR use: Fixed
Invented in the 70’s, big adoption in the 90’s

## Slide 6: Traditional LPR use: Mobile Law

## Slide 7: Traditional LPR use: Parking

## Slide 8: Next Step … Occupancy

## Slide 9: How well does LPR work?
“Our system will read 99% of plates.” *
Exception may include: Plates that do not have a reflective coating or that lost their reflective coating. Plates with physical damages (cracked, bent, dented, stretched …) that distort characters or spaces. Plates that are damaged such that they do not retain an overall rectangular shape. Plates that may be physically obscured from the LPR camera. Plates with non-standard fonts or non-standard spacing. Plates with fixtures that distort characters or spaces. Plates that have been captured more than once. Plates with fixtures that touch characters. Plates that are extremely dirty. Specialty interest plates. False positive plates that are triggered by an environmental item other than a vehicle plate, such as a fence or bumper sticker, are considered to be illegitimate plates
*

## Slide 10: Challenges with LPR as a data collection tool
Properly installed and calibrated system.
Parking vs Law vs Street Sweeper

## Slide 11
Single Plate Vehicles backed in

## Slide 12: What about climate ?
Notes:   Desired enforcement type
  45, 90, parallel
  One or both sides, simultaneous
  Day night
  Climate

## Slide 13: Variety of plates to be read
French plate
Spanish plate
Greek plate
Italian plate

## Slide 14: Variety of plates to be read
Oregon plate(s)
+ 10

## Slide 15: Damaged Plates

## Slide 16: Plates we will always miss

## Slide 17: What about Location?
Enhanced options can increase this significantly, in some cases to < 1”!
GPS (Global Positioning System) can vary from 3 to 30 ft.

## Slide 18: GPS is not always an option

## Slide 19: The Kimley-Horn Pilot Study

## Slide 20: LPR as a Data Collection Tool
What Makes LPR an Effective Option?
    Mobile mounted
    Gathers data related to vehicle presence
    Stores data geospatially and quantitatively
    Opportunities for occupancy and duration

## Slide 21: The Kimley-Horn Pilot Study
6 month pilot study, conducted in:
  Tempe, AZ; Phoenix, AZ; Fort Collins, CO; Houston, TX; Beverly Hills, CA
Purpose of the pilot study was to determine:
  Challenges
  Opportunities
  Accuracy
  Efficiency
  Staff power requirements

## Slide 22: General Parameters of the Pilot Test
Early Phases:
  Conducted in Arizona at KH office and Tempe parking system
  Define protocols for data collection processes
  Test the accuracy of the system
  Determine efficiency and limitations

## Slide 23: The Data Collection Process

## Slide 24: Early Challenges
Front and back license plates (or lack thereof…)
Custom license plates
Melted license plates

## Slide 25: General Parameters of the Pilot Test
Mid Phases:
Conducted in Tempe and Colorado State University parking systems
Improve performance by overcoming challenges
  Add manual counting for backed-in cars with no license plates
  Work with vendor to code new license plates
Determine efficiency of “traveling calibration”

## Slide 26: The “AH HA” Moment
Facility | Manual Count | LPR | Accuracy
City Hall Garage | 239 | 229 | 96%
Brickyard Garage | 674 | 611 | 91%
Surface Lots | 173 | 160 | 92%
Centerpoint Garage | 254 | 258 | 102%
Average |  |  | 95%
Facility | Manual Count | LPR | Accuracy
City Hall Garage | 245 | 160 | 65%
Brickyard Garage | 170 | 138 | 81%
Surface Lots | 78 | 61 | 78%
Centerpoint Garage | 733 | 468 | 64%
Average |  |  | 72%
The addition of manual counting of backed-in vehicles nailed the accuracy of the system
When traveling to locations with front and back license plates, accuracy was stellar
Notes: Arizona does not require a front license plate
Test 1 – LPR do all the work
Test 2 – we included backed in vehicles with the counts
Also tested in Houston, Fort Collins, and Beverely Hills – which require front and back license plates, and we were getting similar accuracy percentages
Also, notice 102%, LPR may collect a random sign that you’ll pass or a logo on a car, but, after a full day of data, these anomalies will normalize

## Slide 27: Mid-Pilot Challenges
How do we actually use this data?
    Reports from back-end system were configured for enforcement
    No easy way to define parking occupancy from reports
    Geospatial tool was helpful for on-street and surface lots

## Slide 28: General Parameters of the Pilot Test
Final Phases:
Conducted in Tempe, Houston, Beverly Hills
Develop reporting and analysis mechanism
  Use existing parameters within back-end reporting to “trick” reports to provide occupancy
  Automate reporting
Test staffing theory’s with non-KH staff
  Parking management staff in Houston
  Parking enforcement staff in Beverly Hills

## Slide 29: Effective Reporting Tools

## Slide 30: How do WE use the data?
Park+ Modeling
    Scenario Planning Tool
Use for Data:
    Calibrating models for communities
    Evaluating event scenarios
    Defining new demand projections
    Maintaining and updating models

## Slide 31: Final Pilot Results
Each test presented a unique challenge… with an equally unique solution
Staff power estimates showed a reduction of up to 50% for most efforts
    Meaning more data can be collected in the same time and budget as previous efforts
Data accuracy was within acceptable levels for our purposes
We are the proud owners of an LPR unit that finds itself all over the country…

## Slide 32: Practical Applications

## Slide 33: Asheville, NC
~15,000 parking spaces
Collection of on-street and off-street occupancy
Comparison of demand collections from 2007, 2010, and 2014
Notes: One analyst, two days for collection process
One day for post processing

## Slide 34: Atlanta, GA
Update of previous occupancy study from 2008
Collected parking data at 30+ parking facilities over a 3 day span
Determine average and overall peaks
Notes: Two analysts, three days for collection process
One day for post processing

## Slide 35: Miami, FL
Hourly on-street occupancy data collection in support of performance-based pricing evaluations
Data collected allowed the project team to determine user characteristics and derive policy recommendations

## Slide 36: Denver, CO
Evaluate parking behavioral characteristics in Prospect Park neighborhood
Occupancy, duration, movement, and appropriate usage

## Slide 37: Using Geospatial Analysis to Improve Studies

## Slide 38: Enhancing the Process

## Slide 39: Improving the Technology for Everyone

## Slide 40: How Can Everyone Use LPR for Data Collection
    Work with your vendor to configure specific reports
    Identify critical data points and work to define how to report for useful analysis
    Determine routing and process as part of regular collection efforts
    Identify key data points to use as benchmarks for program evaluation
    Use data to manage and evolve program

## Slide 41: Questions?
Brett Wood, P.E., CAPP
brett.wood@kimley-horn.com
919-412-0145